# PATTON ELECTRONICS

Patton Electronics Company Model 3120 Remote Access Server V.92 Beta Release 3.4.1BB Jul 3 2002 09:15:26

# Product Specification

### Software Release Overview

The information below gives a basic overview of our current implementation regarding the four features of v.92 modulation. This version of v.92 code is for the purpose of early performance evaluation and BETA field trials. We are currently working closely with several modem manufacturers to continue to hammer out the issues with the remaining features.

- Quick connect (Short phase 1 and 2)

This feature is supported with all three major chipsets.  With the Zoom modem, the command AT+PSS=1 may need to be used for the modem to quick connect.  K56flex needs to be disabled on the server side in order for quick connect to work with Supra.  Connection times are reduced up to 5 seconds.  Short phase 3 and 4 will be supported in the future, which can reduce the connection time to 10 seconds.

- Modem-on-hold

This feature is supported with all three major chipsets.  Call waiting must be enabled on the phone line as well as the modem for this to work.  In some cases, call waiting is disabled on the modem by default.  This must be enabled by entering the command AT+PCW=1.

- PCM upstream

This feature is currently only supported with USR; however, upstream data rates much higher than v.34 cannot be achieved. This is an issue for both server and client modem manufacturers to resolve.  Zoom and Supra still have issues with their PCM upstream.  If anything besides a USR modem is connecting to our RAS, PCM upstream will be disabled automatically for that particular client. This will eliminate any problems we have with PCM upstream.

- v.44

We successfully negotiate v.44 with any modulation.  There is still a small issue remaining with v.44.  If both instances of a DSP have calls on them, throughput is reduced if one or both of the calls are using v.44.

### FEATURES ADDED IN THIS RELEASE

- Automatic refresh rate field – The dial in refresh is currently active on the Dial In page only.  If you would like to configure this feature you will find the settings on the System page.

- V.59 Functionality – Enable/Disabled Switch for this version for testing speeds and throughput.  Some Radius applications were receiving errors due to the previous version of code.  This is a feature used for debugging. Should be disabled unless otherwise instructed by support.

- Quick Connect – Quick has been demonstrated in this release. Short phase 1 and short phase 2 are supported.  This is enabled by selecting quick connect enable on the dial in settings page.

- V.44 Compression – Working successfully with a single call

- PCM-Upstream – USR is currently the only manufacturer with this ability.

- Modem On Hold – Has been demonstrated with this release with all three major chipsets.

- v.92(22) - Will display on the dialin page under modulation when the client modem is v.92 compatible.

- moh (23) - Will display on the dialin page under modulation when the link is on hold due to an incoming call

- DNIS – Dialed Number Identification Service. This feature in its current implementation allows the RAS administrator to setup policies for clients based on the phone number the client has dialed or the WAN port they have come in on.

### v.92 MODEMS TESTED

USR Performance Pro Internal v.92 *- v.92 connection established.

- Quick Connect – Demonstrated

- Modem On Hold –  Application hangs. Modem stalls and hangs up

- v.59 Disable/Enable demonstrated.

- PCM Upstream Demonstrated using USR ControlCenter only.

USR Faxmodem External  v.92 *- v.92 connection established.

- Quick Connect – Demonstrated

- Modem On Hold – Fully functional

- v.59 Disable/Enable demonstrated.

- PCM Upstream Demonstrated using USR ControlCenter only.

Zoom Internal 3025 Faxmodem PCI v.92 “L” chip - v.92 connection established.

- Quick Connect – Demonstrated

- Modem On Hold – Fully functional

- v.59 Disable/Enable demonstrated.

- PCM Upstream – Not supported by manufacture to date.

Zoom Internal  3025 Faxmodem PCI v.92 “N” chip - v.92 connection established.

- Quick Connect  - Demonstrated

- Modem On Hold – Fully functional

- v.59 Disable/Enable demonstrated.

- PCM Upstream – Not supported by manufacture to date.

Zoom Internal  3025 Faxmodem PCI v.92 “C” chip - v.92 connection established.

- Quick Connect  - Demonstrated

- Modem On Hold – Fully functional

- v.59 Disable/Enable demonstrated.

- PCM Upstream – Not supported by manufacture to date.

- Supra SST internal v.92  - v.92 connection established.

- Quick Connect  - Demonstrated

- Modem On Hold – Fully functional

- v.59 Disable/Enable demonstrated.

- PCM Upstream – Not supported by manufacture to date.

- Hayes Accura External v.92 - v.92 connection established.

- Quick Connect – Extremely long v92 negotiation times

- Modem On Hold – No application available from the manufacturer

- v.59 Disable/Enable demonstrated.

- PCM Upstream – Not supported by manufacture to date.

Supra Max USB v.92 - Beta software release and we are currently testing.

- Quick Connect – Demonstrated

- Modem On Hold – Fully functional

- v.59 Disable/Enable demonstrated.

- PCM Upstream – Not supported by manufacture to date.

* Often the USR modems would disconnect after attempting to renegotiate. This occurs only when the modem has established a v92 connection. We are currently trying to determine the reason this occurs.

### Modems tested with known issues

Creative V.90 modem (model DE5625)

Broadxant/Creative PCI V.92 modem (model DI3631)

USR PCI Performance Pro Modem (5610A)

USR External (Model 5686D)

SupraMAX PCI V.92 modem (model 2751)

### v.90 MODEMS TESTED

Micro Modem 56K PCI Fax/Modem

3Com US Robotics Performance Pro 56k PCI Fax/Modem

3Com US Robotics Faxmodem 56k PCI

Diamond Supra 56k USB

Diamond Supra Express 56k USB

Phoebe External 56k USB

D-Link DSB 560 56k USB

H&P Pegasus 56k USB

3Com US Robotics Modem 56k PCMCIA Card

Hayes Accura Faxmodem 56k PCMCIA

Xircom Real Port Ethernet/Modem 56k PCMCIA

Viking WinModem 56k PCMCIA

Single Point Fax Modem 56k PCMCIA

### PROBLEMS RESOLVED IN THIS RELEASE

#2253 – Success banner does not appear for text logins

#2765 – AT&T Q931 Service Ack message is not built correctly

#2478 – frame relay in network mode violates the q933 spec

#2859 - When the compression is set to v.42bis, only v.42bis will be used.  Before, even if the compression was set to v.42bis, v.44 would be negotiated if available.

### OUTSTANDING PROBLEMS

# 940     Add DAX to RS-232 page for configuration at Remote POP’s

#1587 	Communication Problems with certain Telecom Switches

#1759 	Not sending proper tone for PRI busy out

#2041   SLIP is not supported in this release

### COMPLIANCE

- Emissions

FCC Part 15, Class A

EMC Directive 89/336/EEC

- Safety

Complies with UL1950 (MET)

Canadian cMET

Low Voltage Directive 73/23/EEC (EN60950)

- Telecom

FCC Part 68 (testing complete, pending reply from FCC)

Canadian CS-03

CTR-4

Other

Year 2000

NOTE:	This states the compliance of the software when installed in a hardware unit, which has also been certified to be compliant.

### PSTN T1/E1/PRI INTERFACE

- E1 Framing

Common Channel Signaling (CCS)

Double Framing

G.704 with and without Cyclic Redundancy Check (CRC4)

G.704/TS16 with and without CRC4

- E1 Line Encoding

Alternate Mark Inversion (AMI)

HBD3

- E1 Signaling

MFR2 with configurable signaling codes

PRI Switch Support: NET5/CTR-4, TS014, INS1500

Q.931 (Primary Rate Interface - PRI)

- T1 Framing

ESF (Extended Super Frame)

D4 (Super Frame)

NO UNFRAMED G.703

- T1 Line Encoding

Alternate Mark Inversion (AMI)

Bipolar 8 Zero Substitution (B8ZS)

T1 Facilities Data Link

ANSI, T1.403

Disabled by user

Automatically disabled when using Q.931 or Frame Relay

- T1 Signaling

Robbed Bit (Ground Start, Loop Start, E&M Wink, E&M Immediate, Taiwan R1)

Office side robbed bit simulation

PRI Switch Support: NI1, AT&T/Lucent, DMS

PRI terminal equipment side only

Q.931 (Primary Rate Interface - PRI)

T1/E1 Near- and Far-end Statistics (96 intervals of 15 minutes)

Errored Seconds

Severely Errored Seconds

Severely Errored Frame Seconds

Unavailable Seconds

Controlled Slip Seconds

Path Code Violations

Line Errored Seconds

Bursty Errored Seconds

Degraded Minutes

Line Code Violations

Assignments of Individual Timeslots

Off (designates ignore slot)

Dialin (forwards slot to the dialin call manager)

Drop & Insert (passes slot through to the secondary T1/E1)

Frame Relay (groups slot with other frame relay slots on T1/E1)

Blocked (informs PSTN that voice channel is busy)

### DSP RESOURCE POOL

- DSP's Managed as a Pool

Dual Instance DSPs

Automatic detection of installed DSP pool side (12, 24 or 30)

User selection of DSP allocation (all on primary OR split between primary/secondary)

Dynamic loading of modulation/protocol onto next available DSP

Detection of failed DSP's and removal from DSP resource pool

Round Robin allocation of DSP resources

Administrative request to remove a specific DSP from the pool

Stack overflows generate an automatic DSP reboot

DSP diagnostics to reboot and test DSP's while alive

- Analog modulations supported

- V.90 (28,000 - 56,000)

- K56 Flex (32,000 - 56,000)

- V.34 Annex 12 (2,400 - 33,600)

- V.34 (2,400 - 28,800)

- V.8 (capabilities negotiations)

- V.32bis (7,200 - 14,400 with trellis encoding)

- V.32 (4,800 & 9,600)

- V.22 (600, 1,200, & 2,400)

- V.22bis (600, 1,200, & 2,400)

- V.21 (300 bps)

- Bell 212A (1,200 bps)

- Bell 103 (300 bps)

- Bell 202 (75/1,200 bps)

- EIA PN-2330 and low-speed data modem automode procedures

- Modulation supervision for automatic rate selection

- Bit error performance monitoring for automatic fallback and fallforward

Analog Protocols Supported

V.14 synch to async conversion (buffered/direct)

V.42 synch to async conversion with error correction

V.42bis compression

Async Point-to-Point Protocol (PPP), escaping and checksum in DSP

Multilink PPP

Auto detection of PPP or text at login time

Digital physical layers supported

64K HDLC

NO V.110 rate adaptation

NO 56K HDLC

Digital protocols supported

Synchronous Point-to-Point Protocol (PPP)

Multilink PPP

NO V.120 synch to async conversion with error correction

### TCP/IP PROTOCOL SERVICES

Routing

User entry of static routes (gateway/host/interface)

Routing Information Protocol (RIP) Version 1 and Version 2

RIPv1 backwards compatible, reception to either

RIP blocked on dialup lines

Multiple RIP interfaces

ICMP redirect

Address Resolution Protocol (ARP)

Normal ARP on LAN interface

LAN ARP proxy of dynamic dialup IP addresses

ARP proxy even if LAN and dialup pool on different nets

LAN IP Address

User static defined with submask

Reverse Address Resolution Protocol (RARP) at boot up

NO BOOTP

NO DHCP

LAN IP used as network node ID

Management

Support MIB II

Enterprise expansions for IP pool and LAN address

### DIALIN CALL MANAGER

User Login

Selection of None, Text, PAP, PAP/CHAP, CHAP, or auto

Autoselection for text prompt with PPP detection

User modification of all prompts and banners

Special escapes in success banner for IP address and MTU

Username and password information forwarded to Authentication Manager

Text Dialin Connections

Analog calls only

Telnet to remote host

Rlogin to remote host

TCP clear connection to remote host

Remote host IP and port provided as default or through Authentication Manager

Framed dialin connections

Async Point-to-Point Protocol (PPP) on analog calls

Synch Point-to-Point Protocol (PPP) on digital calls

Multilink PPP with Multi-chassis support (L2TP based)

IP address from local pool or Authentication Manager

LCP with address/ protocol field compression and magic number

IPCP with Microsoft Windows 95 extensions for DNS and WINS addresses

Van Jacobson TCP header compression on PPP (not on SLIP)

SLIP on analog calls

Session Management

Viewing of active calls

Viewing of previous 15 dead calls

Administrative forcing call offline

User settable login time limit

User settable idle time limit

User settable session total time limit

Time limits can be over-ridden by Authentication Manager

Dial-in dynamic IP address pool management

User settable modulation requirements specific to dialin

### DIALOUT MANAGER

User Login

Connection via Telnet client on remote PC to Telnet server on box

User configurable Telnet port number (default 24 - port 23 reserved for management)

Ability to restrict dialout feature from dialin sessions

Text or no login

User configurable banners and prompts

User configurable maximum session

AT Command Emulation

Limited AT emulation with ATDT, ATH, ATO

ATEXIT or ATLOGOUT to terminate session

DSP resources not allocated until call is actually made

Session Management

Viewing of active sessions

Viewing of previous 15 dead sessions

Administrative disconnect of session

Login time limit set by user

Idle time limit set by user

Session total time limit set by user

Time limits can be over-ridden by Authentication Manager

Modulation requirements specific to dialout set by user

### T1/E1 DROP AND INSERT

Voice Call Pass-through

Connection of primary T1/E1 to PSTN

Connection of secondary T1/E1 to local PBX

Clock on secondary T1/E1 derived from clock on primary T1/E1

Fixed primary/secondary timeslot correlation (not adjustable)

Limited ability to convert between T1 and E1 (consult factory)

All DSP resources allocated to primary T1/E1

Incoming Call Signaling Conversion Ability

Primary loop start to secondary office loop start

Primary loop start to secondary office ground start

Primary ground start to secondary office loop start

Primary ground start to secondary office ground start

Primary R2 (Q.421) to secondary R2 (Q.421) transparent to interregister tones

Primary Q.931 to secondary office loop start

Primary Q.931 to secondary office ground start

Outgoing Call Signaling Conversions

Secondary office loop start to primary loop start

Secondary office loop start to primary ground start

Secondary office ground start to primary loop start

Secondary office ground start to primary ground start

Secondary R2 (Q.421) to primary R2  (Q.421) transparent to interregister tones

Primary Timeslot Use Assignment or Incoming Calls

Drop & Insert designated slots are passed to secondary T1/E1

Dialin and other designations are handled by primary T1/E1

### AUTHENTICATION MANAGER

Central Authentication Architecture

Fields authentication requests by the Dialin Call Manager

Fields authentication requests by the Dialout Call Manager

Statistics for accepted and invalid authentication

Radius Client

Supports accounting (enabled by user)

Main and backup server IP address

Separate main and backup addresses for accounting server

Retry timer and counts set by user

UDP port numbers for radius and accounting set by user

NAS identifier (defaults to box IP address) set by user

Statistics for server retries and no responses

Static User Database

Database of over 100 users configurable in box

Users defined by username and password

Session Limit, Service Type, Service IP and Service Port held for each user

### MANAGEMENT SERVICES

- Support of Management Information Base (MIB)

- MIB-II (RFC-1213)

- RIPv2 (RFC-1389)

- DS1 (RFC-1406)

- Ethernet (RFC-1643)

- Patton’s Enterprise

- MIB access at a “monitor” and “superuser” level based on password

- Frame Relay (RFC-1315)

System Diagnostics at Boot Time

All hardware systems tested

No external signals sent during power-up

Failed DSP resources taken out of service

Rear Panel RS-232 Configuration Port

VT100 terminal interface

User selectable display of system errors at various priorities

Multi-level menu pages on a limited number of MIB variables

NO PPP or SLIP through this connection

HTTP Server

On board HTTP server for Web based management

Full web site user interface including graphics held internal to box

Ability to disable web interface

Viewing and setting of all MIB variables

Uses HTTP authentication to validate monitor or superuser administration

Simple Network Management Protocol (SNMP) version 1

MIB extensions provided as patton.mib and 2800.mib

Telnet Configuration Management

VT100 terminal interface

Identical interface to the front panel RS-232 port

Remote Software Upgrade

FTP server in the box can receive new code images

Image internally checksummed and validated before being made permanent

Automatic freeze of system, burning of code, and system reboot

Error Logging System

All system events flow through the error logging system

Logs displayed via front panel RS-232

Logs sent to Unix SysLog daemon (UDP)

Logs sent via SNMP traps to designated IP address

Logs stored internally in volatile RAM

High priority logs stored internally in non-volatile FLASH

Selectable error priority on each logging output

System Health Monitoring

CPU usage monitoring

Hardware watchdog timer system reset if stopped

Software monitoring of task performance and reset if failure

Statistics on memory and buffer consumption

Selection of monitor user privileges

None: removes monitor user

Read Only: monitor may read all objects except passwords

Write User: above plus write access to dialin and drop-and-insert objects

Write User IP: above plus write access to IP, RIP and ICMP items

Write User IP Wan: above plus write access to T1 E1, frame relay and MFR2

Write User IP Wan System: above plus write access to syslog, DSP and actions

Write User IP Wan System Uploads: above plus code upload ability

### FRAME RELAY

WAN interface

Activate Frame Relay on primary and/or secondary T1/E1

User selection of exact time slots for Frame Relay

Selection of Dialin and Frame Relay slots on the same T1/E1

Permanent Virtual Circuits (PVC)

User configurable maximum number of PVC

User selectable 2, 3, or 4 byte DLCI address field formats

Congestion recognition and management

Individual DLCI statistics

User configurable layer 3 parameters

Link Layer (HDLC)

Cumulative link statistics

Current throughput indication (10 second average)

Local Management Interface

rfc1315 compliant

User configurable LMI version: Frame Relay Forum Imp; ANSI T1.617; ITU Q.933

7Limited Network interface capabilities with LMI autoconfig and Bi-directional polling

Online help

### Alarms Interface

Alarm Response

Alarm response outputs

Alarm severity customization

Alarm generation

### DAX

Digital Cross Connect

Timing derived from one circuit

Master and fallback clock customization

Status alarm for master and fallback clock